Beagle Logger ConOps
/Users/Emmet/Projects/DAQ_BBC_Hat/
# Sensors
## IMU - $7.85
STM LSM9DS1TR
I2C interface directly to SBC
Run with EKF ect to give:
- Acceleration Vector
- Yaw rate
- Pitch rate
- Roll rate
## GPS - $19.85
Quecel L80 GPS module
3.3v Supply!!!
Interface Directly via telemetry module, via UART
- GPS Position
- GPS Speed
# Inputs/Micro - STM32F107VCT6

## Optimal GPIO
### I2C1
- PB6
- PB7
### I2C2/UART3
- PB10
- PB11
### SPI2
- PB3
- PB4
- PB5

## 2x CAN
2 CAN Busses! Yew~!
Use the MCP2551 or so, theyre 5v but theres heaps of them!
## 16x ADC
Need to be 5v tolerant, need to have some sort of selector maybe?
## Thermistor Pullups
1 k programmable as per the PULL_x lines and a pMOS
## 4x CPPM
Timers for maybe injectors? :D
## X SPI
Left over pins
## X I2C
Left over pins
# Internal Communications
## ProtoBuff
Available on ARM here