BeagleLogga Calibration
/Users/Emmet/Projects/DAQ_BBC_Hat/
# CAN
Should stay how telemetry is going
# Data
Just going to have a C file with a whole bunch of function templates and #defines to do the parsing. This enables somewhat complex transfer functions as well as lookup table interpolation!
Is it possible to do an array of functions with different definitions? :o
Keep this for the digital inputs too, simplicity
Have this easily accessable to the general user!
eg	float channel1_calib(int32 input_1) {	// ADC Conversion
float scaling_factor = 0.9187;
float offset = 4.434;
return scaling_factor* adc_1 + offset;
}
or:	float channel2_calib(int32 input_2) {	// Look up Table
float lu_table[5] = {0, 0.5, 1.5, 2.5, 5.5};
uint8_t lu_baseline[5] = {0, 100, 200, 300, 400};
return iterpolate( adc_2, u_baseline, lu_table);
}
or:	float channel3_calib(int32 input_3) {	// Digital
if ( input_3 > 1)
return 1;
else
return 0;
}
This isnt overly elegant, but it gives the most amount of power and requires sweet fa coding experience above 1st year!
Will need decent docs, but can be done elegantly.
Could give system defines and constants, ie float toVoltge(uint8 input, uint32 value), sampleRate();