BeagleLogga Communications
/Users/Emmet/Projects/DAQ_BBC_Hat/
# Hardware
Fastest, SPI up to 125 MHz on the Pi! Here!
Continuous Scroll between the two
Rpi as master, just dumping between the two
# ProtoBuf!
Using NanoPB or GPB
Needs a header to delimit messages, ie:
0x42 0x42 <msg length> <crcH> <crcL><PB…..>
CRC might be overkill, maybe a parity, num of 1s, ect
# Messages
## message RPi-to-STM32_data {
enum data_type_e {	CAN_Message = 0;
Analogue_Input =1;
Digital_Input = 3;
}
data_type_e data_type = 1;
uint32 CAN_ID = 2;
uint32 CAN_DLC = 3;
uint32 CAN_data0 = 4;
uint32 CAN_data1 = 5;
uint32 CAN_data2 = 6;
uint32 CAN_data3 = 7;
uint32 CAN_data4 = 8;
uint32 CAN_data5 = 9;
uint32 CAN_data6 = 10;
uint32 CAN_data7 = 11;
uint32 input_no = 12;
uint32 input_value= 13;
uint32 timestamp = 14;
}

## message STM32-to-RPi_setup {
enum setup_type_e {	CAN_Enable = 0;
Analogue_Enable =1;
Digital_Input = 2;
ready_to_start = 3;
}
setup_type_e setup_type = 1;
uint32 sampling_time_us = 2;
uint32 Pullup_Enable = 3;
uint32 CAN_ID = 4;