BeagleLogga_TODO
/Users/Emmet/Projects/DAQ_BBC_Hat/
# CAN
- Verify Pull ups on transciever
- Slew Rate Control
- Swap Tx/Rx? I assumed No!
- Add 120 R to near the connectors
# Power Supplies
3.3v Linear, pad but not populate test!
# Sensors
Add IMU
# Flash
Setup so it can be done via the pi!
# Pi
- SPI Connections
- Flash Connections!